## Slide 1: Functional Verification of OpenHMC
Team Members:
  Alaa Rabie
  Ali Maher
  Mahmoud Mousa
  Mohamed Ahmed
  Mohamed Hosam
  Nada Othman
  Rahma Hamdy
Supervisor: Dr. Ibrahim Qamar
Sponsor: Si-vision

## Slide 2: Content
1- Introduction
2- HMC Architecture & Specs
3- RTL design
4- Verification Plan
5- Testbench Architecture
6- RF Agent
7- AXI Agent
8- HMC Agent
9- Scoreboard
10- Coverage
11- Simulation & Results
12- Conclusion

## Slide 3: Content
1- Introduction
2- HMC Architecture & Specs
3- RTL design
4- Verification Plan
5- Testbench Architecture
6- RF Agent
7- AXI Agent
8- HMC Agent
9- Scoreboard
10- Coverage
11- Simulation & Results
12- Conclusion

## Slide 4: Functional Verification
role and position of functional verification in the cycle of digital IC design flow.
also understand why the HDL language “Verilog” isn’t enough for current requirements of verification of complex designs
why people moved to a new hardware verification language called “SystemVerilog” to build testbenches.
1- Introduction
1/12
We need to understand the following points

## Slide 5: ASIC Digital Design Flow
It can be best explained by a flowchart of the typical steps needed for the fabrication of an IC as shown.
1- Introduction
1/12

## Slide 6: As design complexity increases, better tools are needed which lead to moving to SystemVerilog which is basically Verilog with some added features.
Compatible with Object-Oriented Programming
New data types simplify generating and checking stimulus
Coverage
Transaction level modeling
1- Introduction
1/12
Why systemveriolg instead of verilog ?

## Slide 7: Advantages of building verification environment
The Verification Engineer builds the verification environment to test the functionality of the design.
To make sure the RTL meets all the specs.
By simulating multiple test cases and reporting functional coverage once the first version of the RTL is ready.
If either a bug is found or the design not achieving a spec then report back to design engineer.
1- Introduction
1/12

## Slide 8: Advantages of Discovering bugs at early stage
Discovering any bugs before heading into the synthesis and the backend implementation of the IC is very benefitable for multiple reasons, some of them are.
Easier to find the error and fix the bug.
saving time and money of repeating the flow of fabrication.
Less bugs that end in the hands of the consumer.
1- Introduction
1/12

## Slide 9: The Goal of Functional Verification
no design can be entirely bug free for all scenarios, so verification goal is not to prove that the design is bug-free
the process of chip fabrication is very time consuming and costs millions due to designs’ complexity
So discovering any defects at early stage saves time and cost
our focus is about to make sure the design can accomplish its task successfully according to specifications.
1- Introduction
1/12

## Slide 10: The Features of UVM
Universal verification methodology (UVM) is a standard to enable faster development and reuse of verification environments and verification IP throughout the industry.
It’s a library of basic open-source classes we don’t have to know everything about but just include it and extend from it while writing our testbench.
1- Introduction
1/12

## Slide 11: Some of the built-in UVM classes is shown
1- Introduction
1/12

## Slide 12: Goals of the project
Our goal at the end of this project is to build a UVM verification environment for OpenHMC controller RTL design.
1- Introduction
1/12

## Slide 13: Project Objectives are:
Learn Verilog and SystemVerilog programming languages.
Learn OOP.
Understand basic and advanced verification skills and flow.
Developing codes of a UVM environment.
Learn how to read a specification file.
Learn how to read user manual of a simulation tool.
1- Introduction
1/12

## Slide 14: What’s OpenHMC?
Features.
Supported Confugurations.
1- Introduction
3/12

## Slide 15: Content
1- Introduction
2- HMC Architecture & Specs
3- RTL design
4- Verification Plan
5- Testbench Architecture
6- RF Agent
7- AXI Agent
8- HMC Agent
9- Scoreboard
10- Coverage
11- Simulation & Results
12- Conclusion

## Slide 16: Interfaces, pins and configuration parameters
2-HMC Architecture & Specs
2/12

## Slide 17: Configuration parameters
2/12
2-HMC Architecture & Specs

## Slide 18: Interfaces and Pins
2/12
2-HMC Architecture & Specs
We ’ve 5 interfaces:
AXI
HMC Physical Layer (transceiver) interface
System Interface
HMC Interface
Register File Interface
Interfaces

## Slide 19: AXI Interface
2-HMC Architecture & Specs
2/12
What’s AXI ?
AXI-Interface Pins
TVALID [1 bit]
TDATA [FPW*FLIT_SIZE]
TUSER [NUM_DATA_BYTES bit]
TREADY [1 bit]

## Slide 20: Other Interfaces
HMC Physical Layer (transceiver)
Interface.
System Interface.
HMC Interface.
2-HMC Architecture & Specs
2/12

## Slide 21: Register File Interface
2-HMC Architecture & Specs
2/12
What’s its usage?
How to get data from it?
Its contents and address
map.

## Slide 22: TS1 (Training Sequence)
2-HMC Architecture & Specs
2/12

## Slide 23: Transaction and Link Layers
Difference between Transaction
and Link layers.
What are Flow packets?
Transaction layer packets.
2-HMC Architecture & Specs
2/12

## Slide 24: Link Retry
When is it triggered?
Retry Buffer.
Forward Retry Pointer (FRP).
Return Retry Pointer (RRP).
RETRY POINTER RETURN (PRET) packet.
2-HMC Architecture & Specs
2/12

## Slide 25: Transaction layer: Packet Flow Control
What’s it?
How is it managed? (TRET)
2-HMC Architecture & Specs
2/12

## Slide 26: Transaction layer: Request Packets
Request Header Layout.
Request Tail Layout.
2-HMC Architecture & Specs
2/12

## Slide 27: Transaction layer: Response Packets
Response Header Layout.
Response Tail Layout.
2-HMC Architecture & Specs
2/12

## Slide 28: Transaction layer: Request Commands
READ and WRITE Request Commands.
POSTED WRITE Request Commands.
MODE READ and WRITE Request Commands .
BIT WRITE Command.
2-HMC Architecture & Specs
2/12

## Slide 29: Transaction layer: Response Commands
READ and MODE READ Response Commands.
WRITE and MODE WRITE Response Commands.
ERROR Response Command .
2-HMC Architecture & Specs
2/12

## Slide 30: Link layer: Flow Commands
NULL Command.
RETRY POINTER RETURN (PRET) Command.
TOKEN RETURN (TRET) Command.
INIT RETRY (IRTRY) Command.
2-HMC Architecture & Specs
2/12

## Slide 31: Transaction Layer Initialization
NULL FLITs.
TS1 patterns.
NULL FLITs.
TRET packets.
Request/Response packets.
2-HMC Architecture & Specs
2/12
/12

## Slide 32: Content
1- Introduction
2- HMC Architecture & Specs
3- RTL design
4- Verification Plan
5- Testbench Architecture
6- RF Agent
7- AXI Agent
8- HMC Agent
9- Scoreboard
10- Coverage
11- Simulation & Results
12- Conclusion

## Slide 33: Module Description
Transmit and Receive FIFOs.
TX Link (tx_link.v).
RX Link (rx_link.v).
Register File (openhmc_rf.v).
Header File.
Top Module (openhmc_top.v).
3- RTL design
3/12

## Slide 34: Module Description: TX Link
FSM.
3- RTL design
3/12

## Slide 35: Module Description: RX Link
FSM:
  HMC Down.
  HMC wait for NULL.
  HMC NULL.
  HMC TS1 part Align.
  HMC TS1 find ref.
  HMC TS1 align.
  HMC NULL Next.
  HMC Up.
3- RTL design
3/12

## Slide 36: Content
1- Introduction
2- HMC Architecture & Specs
3- RTL design
4- Verification Plan
5- Testbench Architecture
6- RF Agent
7- AXI Agent
8- HMC Agent
9- Scoreboard
10- Coverage
11- Simulation & Results
12- Conclusion

## Slide 37: Verification Plan sheets
4- verification Plan
4/12
Design requirement.
system sheet.
Interfaces sheet.
Generation sheet.
Checking sheet.
Test list sheet.
Rf map sheet.

## Slide 38: Design Requirements
4- verification Plan
4/12
This sheet contains
  the features of the
  design specs.

## Slide 39: System Sheet
This sheet contains
  Approach.
4/12
4- verification Plan

## Slide 40: Interfaces Sheet
This sheet contains
  Approach.
  Component name.
  Notes.
4- verification Plan
4/12

## Slide 41: Generation Sheet
This sheet contains
  Generation.
  Component name.
  Extends.
4- verification Plan
4/12

## Slide 42: Checking Sheet
This sheet contains
  Approach.
  Check.
  Check type.
  Comment.
4- verification Plan
4/12

## Slide 43: Coverage Sheet
This sheet contains
  Covergroup.
  Coverpoint.
  Cross.
4- verification Plan
4/12

## Slide 44: Test List Sheet
This sheet contains
  Test name.
  Sequence run.
  Stimulus generated.
  Notes.
4- verification Plan
4/12

## Slide 45: RF Map Sheet
4- verification Plan
4/12
This sheet contains
  the register file address map and its contents.

## Slide 46: Content
1- Introduction
2- HMC Architecture & Specs
3- RTL design
4- Verification Plan
5- Testbench Architecture
6- RF Agent
7- AXI Agent
8- HMC Agent
9- Scoreboard
10- Coverage
11- Simulation & Results
12- Conclusion

## Slide 47: Testbench Architecture
5- Testbench Architecture
5/12

## Slide 48: Main Code Files
tb_top module
  Import all testbench packages.
  Instantiation of all the interfaces and the design top module.
  Bind assertions file.
  Generation of the clock.
5- Testbench Architecture
5/12

## Slide 49: Main Code Files
Packages
  cmd_pkg
  axi_pkg
  hmc_agent_pkg
  rf_reg_block_pkg
  rf_agent_pkg
  tb_params_pkg
5- Testbench Architecture
5/12
Packages
  cmd_pkg
  axi_pkg
  hmc_agent_pkg
  rf_reg_block_pkg
  rf_agent_pkg
  tb_params_pkg
  seq_pkg
  test_pkg

## Slide 50: Main Code Files
Environment
Configuration Class
System Interface
5- Testbench Architecture
5/12

## Slide 51: Main Code Files
5- Testbench Architecture
5/12
hmc_pkt_item class
  Define packet fields
  Set constraints regarding each field
  Pack and unpack functions
  CRC calculation

## Slide 52: Main Code Files
5- Testbench Architecture
5/12
Other Interfaces and Agents
AXI-Agent
RF-Agent
HMC-Agent

## Slide 53: Content
1- Introduction
2- HMC Architecture & Specs
3- RTL design
4- Verification Plan
5- Testbench Architecture
6- RF Agent
7- AXI Agent
8- HMC Agent
9- Scoreboard
10- Coverage
11- Simulation & Results
12- Conclusion

## Slide 54: Method of Implementation
Build a register model that maps all the DUT’s registers
  Separate class for each register
  Group the registers into a register block
  Create an adapter as a bridge between the agent and RF model
6- RF Agent
6/12
Common method called “RAL” in UVM cookbook

## Slide 55: Registers
UVM already has built-in classes
  uvm_reg
  uvm_reg_field
6- RF Agent
6/12

## Slide 56: Register Block
uvm_reg_block
And a uvm_reg_map
6- RF Agent
6/12

## Slide 57: Adapter
Convert from the uvm register sequence item into the item used to communication with the interface
Extends from uvm_reg_adapter
6- RF Agent
6/12

## Slide 58: Interface Assertions
Written 4 concurrent assertions
6- RF Agent
6/12
Assertion Name | Explanation
no_simultaneous_read_and_write | As stated in the design documentation, the read enable and write enable signals must not be asserted at the same time, so the register file accepts only 1 operation at a time to access it. Either read or write
invalid_address_assert_if_wrong_write_operation | Inside of it written all the addresses that its registers are read-only, so if write enable signal is asserted with these registers’ addresses the invalid address signal should be asserted
invalid_address_assert_if_wrong_read_operation | Same as above but for the 1 register that is write only
access_complete_one_cycle_after_operation | By testing and as shown in the design documentation, access complete signal is always asserted after 1 clock cycle of asserting read or write enable

## Slide 59: Bad Documentation
2 of the registers’ description in the design documentation is different from how they are implemented in the RTL
6- RF Agent
6/12
Control Register
Counter Reset

## Slide 60: Sequences
Initialization sequence
Sleep sequence
Wrong operations sequence
Read and reset sequences
6- RF Agent
6/12

## Slide 61: Initialization Sequence
Configure the DUT
6- RF Agent
6/12
Wait for rx ready
Wait for link up

## Slide 62: Sleep Sequence
Implemented to cover a certain scenario in the DUT
6- RF Agent
6/12
Will lower the LxRXPS pin then the other side will also enter sleep mode and lower LxTXPS
Then exit sleep by lowering set_hmc_sleep and then the DUT assert LxRXPS and wait for the other side to assert LxTXPS
  Means it will enter the WAIT_FOR_HMC state

## Slide 63: Content
1- Introduction
2- HMC Architecture & Specs
3- RTL design
4- Verification Plan
5- Testbench Architecture
6- RF Agent
7- AXI Agent
8- HMC Agent
9- Scoreboard
10- Coverage
11- Simulation & Results
12- Conclusion

## Slide 64: AXI agent architecture
7- AXI Agent
7/12

## Slide 65: AXI Interface
7- AXI Agent
7/12

## Slide 66: hmc_pkt_item_request
7- AXI Agent
7/12

## Slide 67: valid_data
Encapsulates two signals:
It is the sequence item that the sequencer sends to the driver.
7- AXI Agent
7/12

## Slide 68: Driver
Drives the signals to the DUT via the interface.
7- AXI Agent
7/12

## Slide 69: Sequence
7- AXI Agent
7/12
Generate request packets of type hmc_pkt_item_request
Assign tags to the packets
Divide the packets to flits
Create a valid_data item and arrange the flits to form TDATA with maximum 4 flits and assign TUSER
Send the valid_data items to the sequencer

## Slide 70: Monitor
request analysis port
response analysis port
7- AXI Agent
7/12

## Slide 71: Content
1- Introduction
2- HMC Architecture & Specs
3- RTL design
4- Verification Plan
5- Testbench Architecture
6- RF Agent
7- AXI Agent
8- HMC Agent
9- Scoreboard
10- Coverage
11- Simulation & Results
12- Conclusion

## Slide 72: HMC Agent
Reactive agent.
Has 3 components:
  Driver.
  Monitor.
  Sequencer.
2 Stages.
8- HMC Agent
8/12
Initialization
Stage
Request/Response
Stage

## Slide 73: Initialization Stage: Driver
TX and RX state in the DUT.
packing_FLITS() function.
NULL State.
TS1 State.
8- HMC Agent
8/12

## Slide 74: Initialization Stage: Monitor
“notify_req_transaction” function.
“notify_res_transaction” function.
8- HMC Agent
8/12

## Slide 75: Initialization Stage: Sequences
hmc_init_vseq.
  hmc_state_seq.
  hmc_initialization_seq.
8- HMC Agent
8/12

## Slide 76: Request/Response Stage: Driver
“write_request” function & “request_queue”.
link_status class.
“link_up” function.
“get_packets” function.
“get_response” function.
8- HMC Agent
8/12

## Slide 77: Content
1- Introduction
2- HMC Architecture & Specs
3- RTL design
4- Verification Plan
5- Testbench Architecture
6- RF Agent
7- AXI Agent
8- HMC Agent
9- Scoreboard
10- Coverage
11- Simulation & Results
12- Conclusion

## Slide 78: Scoreboard
A UVM scoreboard receives transactions from a monitor
Predicts what DUT outputs should occur based on DUT inputs
Receives transactions containing the values driven into the DUT.
Calculates what the DUT outputs should be for those inputs.
Stores the predicted results until the actual DUT outputs are available.
9- Scoreboard
9/12

## Slide 79: Scoreboard
Receives transactions containing the values of the actual outputs.
Compares the actual outputs to the predicted outputs.
9- Scoreboard
9/12

## Slide 80: Scoreboard goals
We check that if :
  the received packet is the transmitted packet
  the response packet is the expected response packet
  of the request packet.
9- Scoreboard
9/12

## Slide 81: Scoreboard functions
9- Scoreboard
9/12

## Slide 82: report phase
finally report
  the result of comparison to know that where the error has happened
  Number of axi4_req_packet.
  Number of axi4_rsp_packet.
  Number of hmc_req_packet.
  Number of hmc_rsp_packet.
  Number of error_response.
9- Scoreboard
9/12

## Slide 83: Content
1- Introduction
2- HMC Architecture & Specs
3- RTL design
4- Verification Plan
5- Testbench Architecture
6- RF Agent
7- AXI Agent
8- HMC Agent
9- Scoreboard
10- Coverage
11- Simulation & Results
12- Conclusion

## Slide 84: Coverage
Coverage Measure verification progress
Types of coverage :
  code coverage.
  Functional coverage.
10-Coverage
10/12

## Slide 85: code coverage
Automatically extracted from design code.
measures how much of the design code is exercised.
Tool generated.
usually used to identify holes in the verification that has been performed.
Sometimes called structural coverage.
10-Coverage
10/12

## Slide 86: code coverage
Has many types
10-Coverage
10/12
Code coverage
Statement coverage
Expression coverage
FSM coverage

## Slide 87
Statement coverage
Statement coverage can also be
called block coverage or line
coverage ,where a block is
a sequences of statements that
are executed if a single statement
is executed .
10-Coverage
10/12
code coverage

## Slide 88: code coverage
Expression coverage
Expression coverage measures the
various way decisions through the code.
10-Coverage
10/12

## Slide 89: code coverage
FSM coverage
FSM coverage has two types :
  State coverage:
  Which states have been visited.
  Transition coverage:
  did all possible transition happen.
10-Coverage
10/12

## Slide 90: what Dose 100 percent code coverage mean ??
The entire design implementation was executed.
It does not provide an indication about the correctness of the verification suite.
That doesn’t mean the design is complete.
what if the designer forget to implement a feature from the specs? would code coverage be affected?
We need Functional coverage.
10-Coverage
10/12

## Slide 91: Functional coverage
Written according to feature from the specs.
Functional coverage is another technology to help ensure that a bad design is not hiding behind passing testbenches. (design tested well.)
Functional coverage records relevant metrics (packet length, instruction op_code, buffer occupancy level , e.g.) to ensure that the verification process has exercised the design through all of the interesting values.
10-Coverage
10/12

## Slide 92: Functional VS code coverage
Code coverage measures how much of the implementation has been exercised, Functional coverage measures how much of the original design specification has been exercised.
High functional coverage does not necessarily correlated with high code coverage.
10-Coverage
10/12

## Slide 93: Functional VS code coverage
10-Coverage
10/12

## Slide 94: Functional coverage
Covergroup
The covergroup construct encapsulate the specification of a coverage model. Each covergroup specification can include the following components:
A clocking event that synchronizes the sampling of the coverage points.
A set of coverage points .
Cross coverage between coverage points .
10-Coverage
10/12

## Slide 95: cross coverage points
cross coverage is specified between the cover points or variables. Cross coverage is specified using the cross construct.
Expression cannot be used directly in a cross, a coverage point must be explicitly defined first .
10-Coverage
10/12

## Slide 96: Content
1- Introduction
2- HMC Architecture & Specs
3- RTL design
4- Verification Plan
5- Testbench Architecture
6- RF Agent
7- AXI Agent
8- HMC Agent
9- Scoreboard
10- Coverage
11- Simulation & Results
12- Conclusion

## Slide 97: Tools
Ran the simulations on Questasim v2021.1
11- Simulation and Results
11/12

## Slide 98: Tests
Simple test
Tests with more constraints
Test to hit HMC_RTRY state
Reset tests
11- Simulation and Results
11/12

## Slide 99: Simple Test
First test to try
Usual sequence of operations then enter and exit sleep mode
11- Simulation and Results
11/12

## Slide 100: Simple Test Results
Functional Coverage
Code Coverage
FSM Coverage
  3 FSMs, 19 states and 37 transitions
11- Simulation and Results
11/12

## Slide 101: Simple Test Results
FSM Coverage
  State
  TX init
  RX init
11- Simulation and Results
11/12
These results gave us motive to test the messing scenarios in the FSMs

## Slide 102: Results
Tested Features
Tested Configurations
11- Simulation and Results
11/12
Features | Tested
Full link-training, sleep mode and link retraining | 
16Byte up to 128Byte read and write (posted and non-posted) transactions | 
Posted and non-posted bit-write and atomic requests | 
Mode read and write | 
Error response | 
Full packet ﬂow control | 
Packet integrity checks (sequence number, packet length, CRC) | 
Fully automatic error handling and link retry | 
Control and detect lane reversal and lane polarity | 
AXI Interface Configurations | Tested
2 FLITs per Word / 256-bit Datapath | 
4 FLITs per Word / 512-bit Datapath | 
6 FLITs per Word / 768-bit Datapath | 
8 FLITs per Word / 1024-bit Datapath | 

## Slide 103: Results
Functional Coverage
Code Coverage
Assertions
11- Simulation and Results
11/12

## Slide 104: Results
FSM Coverage
  State
  TX init
  RX init
11- Simulation and Results
11/12

## Slide 105: Content
1- Introduction
2- HMC Architecture & Specs
3- RTL design
4- Verification Plan
5- Testbench Architecture
6- RF Agent
7- AXI Agent
8- HMC Agent
9- Scoreboard
10- Coverage
11- Simulation & Results
12- Conclusion

## Slide 106: Conclusion
12- Conclusion
12/12
Learned Points.
Faced Problems.
Advices and Future Work.

## Slide 107
12- Conclusion
12/12
  Faced compilation and simulation errors ,that we learned to search for solutions .
  self-learning that we don’t specifically need an instructor
Learned
lessons
1.Learned lessons
  Learned System Verilog ,UVM, functional verification.
  >ALU before starting on our graduation project.
  >(Questasim) and write its scripts.

## Slide 108: 2.Faced Problems
aspects of the design hard to understand as the whole design was explained in about 16 papers only.
  graduated engineers advice us to search for online resources,
  the problem was the only source was the specs document.
2. the verification plan took long time period because of the lack of example
12- Conclusion
12/12

## Slide 109: 2.Faced Problems
Company tool
  moveing files from our devices to the virtual machine was closed.
  copy and paste text was also closed.
    So, if we use this tool we must create new files inside the virtual machine and write all the RTL codes and our Testbench codes.
  No internet connection.
    GitHub
12- Conclusion
12/12

## Slide 110: 3.Advices and Future Work
notes about things we could’ve done through the project
  During compilation and simulation, we faced many errors
    we solve them and save in excel sheet.
  There are many coding and functional verification methods we didn’t try during this project during the lack of time
    trace the RTL code and read each statement, branch or condition that we didn’t hit and try to test it with a scenario.
  3) adding more tests and covergroups as our design is very simple.
12- Conclusion
12/12